European Union Rule of Law Mission in Kosovo

EULEX Kosovo

Ndertesa Farmed

“Muharrem Fejza” p.n.

Lagja e Spitalit

10000 Pristina, Kosovo

www.eulex-kosovo.eu

# CORRIGENDUM (3)

PUBLICATION REFERENCE: PROC/361/12/Residential Security Upgrade Kosovo wide FWC (EuropeAid/133523/L/SUP/XK)

# The following corrections are made to the Annex II+III Technical Specifications:

The technical and financial evaluation of the offers will be made on the basis of these amended Technical Specifications.

| Item No | Former text of the technical specifications | Shall read as new text: (added/amended text in red) |
| --- | --- | --- |
|  | Security Doors Steel metal frame of 60mm x 40mm width. Steel plate 2x2 mm each sides. Security viewing hole Dead bolt lock. Handle Minimum 2 Security locks. Cylinders must meet at least European norm EN 1303 Grade 4. To be equipped with a special protection to prevent wrenching from the outside, of a drill-resistant plate and also to be protected from burglar tools Minimum 3 keys per lock. Compliant to ENV 1627 Class 5, tested according to ENV 1630. Security hinges must be of the anti-rise type must be installed on the inside of the doors (not accessible from outside). | Security Doors Compliant to ENV 1627 Class 3, tested according to ENV 1630 Steel metal frame of 60mm x 40mm width (+/-10mm) Rigid steel sub-frame. Door thickness: minimum 50mm Double-sided whole-area armoring with 1-1.5 mm steel sheet. Armoring reinforced with minimum 4 mm hardened steel sheet in the area of the lock Stainless steel hinges with security dog bolts for security. Security viewing hole Dead bolt lock. Handle. Security door lock must meet at least European norm EN 12209 Grade 3. To be equipped with a special protection to prevent wrenching from the outside, of a drill-resistant plate and also to be protected from burglar tools Minimum 13 security points. Minimum 3 keys per lock. Door size: 90cm (width) x 200cm (length) (wing dimension). Surfaces finish: veneered planks or solid wood panels. |
| 1.1 | Installation of Security Doors Installation of Security Doors – GARDESA with following technical specifications: Steel metal frame of 60mm x 40mm width. Steel plate 2x2 mm each sides. Security viewing hole Dead bolt lock. Handle Minimum 2 Security locks. Cylinders meet European norm EN 1303 Grade 4. Equipped with a special protection to prevent wrenching from the outside, of a drill-resistant plate and also to be protected from burglar tools Minimum 3 keys per lock. Compliant to ENV 1627 Class 5, tested according to ENV 1630. Note: EULEX will provide the Security doors therefore for this item we require only the installation services. | Installation of Security Doors Installation of Security Doors – GARDESA with following technical specifications: Steel metal frame. Steel leaf 18/10mm. Security viewing hole Dead bolt lock. Handle Minimum 3 keys per lock. Door size: min.85cm (width) x max.210cm (length) (wing dimension) Compliant to ENV 1627 Class 3, tested according to ENV 1630. Note: EULEX will provide the Security doors therefore for this item we require only the installation services. |